EnOcean

---
General
- ERP specification defines the structure of a radio telegram
- EEP (equipment profiles) defines the user data in the telegram
- Each device defines 3 profile elements:
  - RORG: telegram type
  - FUNC: functionality of the data content
  - TYPE: type of device

---
Telegram Types
Telegram types are grouped by CHOICE (RORG) number

---
Telegram Types (RPS & 1BS)
- 1 byte payload
- LRN bit is in position DB_0.BIT_3
- T21 = 0 => PTM switch module type 1 (PTM1XX), T21 = 1 => PTM switch module type 2 (PTM2XX)
- NU = 1 => N-message (N = normal)
- NU = 0 => unassigned

---
Telegram Types (4BS)
4 byte payload (bytes reversed)

---
Telegram Types (VLD)
Variable data length

---
Teach-in
- Defines the mutual connection between devices
  - Defines to which transmitter a receiver listens to
- The receiver detects if the device is already learned or unknown from the sender ID
- Different for each telegram type
- Procedure:
  - Receiver into learning mode, each sender ID will then be stored by the receiver
  - The transmitter sends a telegram
  - The bits of the payload can have multiple functions

---
F6: RPS telegram

---
F6-02: Rocker Switch
- 2 message types (identified from the status field) N and U
- Application style 2 also exists, but is typically used in the US and Canada

---
F6-02: Rocker Switch (NU = 1)

---
F6-02: Rocker Switch (NU = 0)

---
D2-01
Electronic switches and dimmers with energy measurement and local control

---
D2-01: Command 0x01
Actuator Set Ouput

---
D2-01: Command 0x02
Actuator Set Local

---
D2-01: Command 0x03
- Actuator Status Query
- Actuator responds with an Actuator Status Response
  - Timeout 300ms

---
D2-01: Command 0x04
- Actuator Status Response (actuator → gateway)
- Sent if: (a) status of one of the channels changes locally or (b) Actuator Status Query is received
- If all channels are requested, separate responses will be sent

---
NodOn In-Wall 2 Channel Module
Profile: D2-01-12